## Slide 1: Touchless muscle activity monitoring for Hand gesture recognition
1
Zijing Zhang,
PhD Candidate,
2019-Expected May 2023,
School of Electrical and Computer Engineering
Cornell University, Ithaca, NY
Notes: Hello, welcome to my A exam. The topic of my presentation is ….

## Slide 2: Existing hand gesture recognition systems
Camera-based?
Occlusion
Complex
Privacy
Latency
Motion-based?
Bulky on finger and hand
Only surface motion
sEMG-based?
Direct skin contact
Ambiguity
Numerous electrodes
Gloved-based?
Hinder hand motion
Inconvenient
Uncomfortable
Notes: Hand gesture recognition (HGR) is a natural and effective way of human-computer interaction (HCI).
Camera based HCI though with high accuracy, requires off-body line-of-sight (LoS) cameras, vulnerable to obstruction from self and ambient. Invlove privacy issue, For dynamic motions, adequate time resolution would demand high frame rates.

## Slide 3: RMG (radio-myography) for muscle activity sensing
Multiple-input multiple-output (MIMO)
near-field coherent sensing (NCS) radio sensor
Touchless
continuous muscle actuation sensing that can be wearable and touchless, capturing both superficial and deep muscle groups.
Notes: From near-field EM coupling, NCS modulates the dielectric change of the internal muscle groups during hand gestures onto radio signals.
Advantages : 1.non-invasive, touchless 2. forearm, not hinder finger motions 3. couple deep muscle groups

## Slide 4: Study protocol and data processing
23 hand gestures used in the study protocol
data pre-processing
8 participants 5,847 samples
23 gestures
Each gesture is segmented into 5s time window
1D time series
To
2D spectrogram
STFT
CWT

## Slide 5: Classification results using deep learning
personal training model
7-fold CV
Model:
Vision transformer
Overall accuracy=99.0%

## Slide 6: Classification results using deep learning
Model:
Vision transformer
Overall accuracy=96.6%
Transfer learning on the unseen participant by 1/5 of new data.
Pre-train on
general model
Fine-tune by
few cases of
new participant

## Slide 7: Analysis on classification results
(a)
(b)
(c)
(d)
personal training model
Transfer learning for unseen users
Vision
Transformer outperformed
CNN
Ensemble
boosts
accuracy
Notes: Attention mechanism enhances the important parts of the input data and fades out the rest. Long-term dependency.

## Slide 8: Benchmark with sEMG
G
+
-
sEMG
RMG and sEMG waveforms for various gestures by DTW averaging on all samples
Exp: | 1 | 2 | 3 | µ
RMG | 99.0% | 98.5% | 98.7% | 98.7%
sEMG | 68.2% | 70.8% | 66.7% | 68.6%
Accuracy comparison
of RMG vs. sEMG
High temporal correlation
Consistent time lag
Notes: Conventional sEMG is the present gold standard in clinical applications for muscle activity detection and electro-diagnosis.
Compared peak location and pulse width
RMG and sEMG have a high temporal correlation and a consistent time lag. This delay may indicate the time offset between neural stimulation and muscle actuation.

## Slide 9: Variation in experimental design
 | Timing Test | 
 | 150 beats/minute | 
 | µ | σ
RMG | 0.40 s | 38 ms
sEMG | 0.40 s | 55 ms
Timing and latency
 | Notch (a) | Box (b) | Wrist (c)
Accuracy (%) | 99.0 | 97.4 | 95.8
Sampling rate:
Camera: 60 fps RMG: 1M sps
Notes: High time resolution with low latency is an important criterion for dynamic HGR.
For camera-based methods, the high time resolution demands high frame rates with increasing cost and heavy data loads,
Conclusion: RMG can capture gestures with high speed with ultra-low latency

## Slide 10: Comparison of RMG to previous HGR works.
Notes: Most of the existing HGR systems can only distinguish fewer than 10 hand gestures.
RMG outperform state-of-art HGR systems regarding gestures we can distinguish and accuracy we can achieve at the same time

## Slide 11: Applications in Human Machine Interface
virtual reality gesture control
Hand gesture recognition system
Smart device control
Virtual object manipulation
Notes: facilitate human computer interaction3D virtual reality control; sign-language detection for disable people, assistive robotic control; non-contact navigation in smart cars .
Eye-movement and blink for gaze control